## Slide 1: BrainSync: Synchronizing Resting State Brains

## Slide 2: rsfMRI data
rsfMRI signals are not directly comparable across subjects because they are out of sync.
We assume that:
  The time series are variance normalized
  The brains have similar overall correlation patterns
  The time series with T-samples can be represented as a point on sphere .

## Slide 3: Metric on fMRI Signal
Y
d
We assume that all the time series are equally likely, i.e.
the sphere has uniform metric
The distance between two time series is given by
where is correlation between and .
X

## Slide 4: Time series of subjects are on spheres
Individual scans are rotated/flipped spheres with respect to each other
Kabsch algorithm is used to find optimal orthogonal transformation between spheres
Finding Optimal orthogonal transformation has a closed form solution based on SVD
…
Sub 1
Sub 2
Sub n

## Slide 5: Finding Optimal Orthogonal Transformation
Problem: We want to find an orthogonal matrix that aligns data and of the two brains
Where , are of the form where is the number of vertices and
number of time points.
Solution:
First, we perform SVD of covariance matrix .
The optimal orthogonal matrix is given by . (details skipped).
This yields and in sync.
The transformed data has the same correlation pattern as the original
It is a 1-1 transform

## Slide 6: Correlation of Signals
Average Correlation in
rfMRIs of original Subjects
Average Correlation in
rfMRIs of BrainSynced Subjects
0
1

## Slide 7: Task fMRI (language task)
2 Subjects were considered without tNLM
Correlation of time series from one subject to the other was computed
Before Sync
After Sync
0
0.15
Correlation of resting state to task fMRI (from different subjects)
are much lower even after Brain Sync

## Slide 8: Correlation of Signals
Correlation of average signal in precuneus to the signals in brain
Sub 1 to Sub 1
Sub 1 to Sub 2 (orig)
Sub 1 to Sub 2 (rot)
0
1

## Slide 9: Parcellation Individually
Subjects were independently parcellated by k-means with nClusters=30
Sub 1
Sub 2
Sub 3
Sub 4
Parcellations are different for individual scans, probably because not enough samples
for finding correct boundaries

## Slide 10: Group Parcellation
Since the data are comparable to each other after BrainSync, we can pool it and do joint parcellation
Clustering will work better when data is pooled, rather than doing clustering of one brain at a time
We can now directly pool the data together after synchronization

## Slide 11: Joint Parcellation 2 independent groups of 20 subjects each
2 subjects from first group
2 subjects from second group
We get more consistent Parcellation even if two groups of 20 subjects are non-overlapping
Therefore Joint clustering must be helping in improving performance of clustering algorithm
since there is more data.

## Slide 12: Session 1 and Session 2 labeled jointly
Subject 1
Session 1
Session 2
Session 1
Session 2
Subject 2
40 Subjects x 2 sessions = 80 scans were pooled together for labeling

## Slide 13: 100 ROIs Joint Clustering
A large number of ROIs also show consistent parcellation when done in a group-wise manner
Sub 1, Session 1
Sub 1, Session 2
Sub 2, Session 1
Sub 2, Session 2
Consistent clustering is obtained even if we haven’t enforced any prior for
similarity across subjects or even boundary smoothness within subject

## Slide 14: 100 ROIs Individual Clustering and recoloring
Sub 1 Sub 2 Sub 3 Sub 4
There is very little consistency across subjects

## Slide 15: Conclusion
Parameter free approach
Depends on only 2 simple assumptions
No Spatial Prior or group prior is assumed, regions can be very different as possible, No constraint on topography of the labels
Purely data driven
Involves clustering of a large amount of data, so scalable algorithm is required (e.g. k-means)

## Slide 16: Brain Registration using fMRI
Original labeled brain for subject 2
We map each vertex of subject 1
to the closest vertex of subject 2 in
the spherical space

## Slide 17: Other Possibilities
Cortical Registration based on fMRI!!
  The distance of sphere can be used to drive registration
  Or the correspondence can be found directly on sphere using Hungarian Algorithm
Group Studies
  We have developed framework for performing statistics on sphere
  After BrainSync these signals are directly comparable
  Group Differences and other studies can be performed easily
Will the results be same if correlation is used as a feature ?
Sparsity priors can be used for fitting the orthonormal transformation